# 地下结构抗震分析中若干土层模拟方法对比研究

### 论文摘要

动力时程在地下结构抗震分析中应用广泛,土体动力特性的准确模拟对动力时程分析结果有重要影响。介绍了Rayleigh阻尼和Hardin-Drnevich模型的基本理论,验证了等位移边界条件的有效性。从地表加速度响应和加速度幅值沿深度放大两方面,对比分析Mohr coulomb模型、Shake91、Rayleigh阻尼和Hardin-Drnevich模型在2Hz和8Hz正弦波作用下的响应结果。结合理论分析得出:静力Mohr coulomb模型对动力时程分析适用性有限;建议在地下结构抗震分析中采用场地基频与接近地震波主频固有频率计算Rayleigh阻尼参数;Hardin-Drnevich等粘弹性非线性模型比等效线性化方法更适用于地下结构抗震分析。

### 论文目录

- 引言

- 1 土层模拟

- 1.1 时域等效线性化

- 1.2 Hardin-Drnevich模型

- 2 数值算例

- 2.1 边界条件

- 2.2 模型参数

- 2.3 土体模拟参数

- 3 有限元结果及分析

- 3.1 有限元结果

- 3.1.1 正弦波2Hz

- 3.1.2 正弦波8Hz

- 3.2 分析与讨论

- 3.2.1 Mohr coulomb的适用性

- 3.2.2 Rayleigh阻尼误差

- 3.2.3 等效线性方法与Hardin-Drnevich模型差异

- 4 结论

### 文章来源

类型: 期刊论文

作者: 杨喻声,禹海涛,袁勇

关键词: 动力时程,阻尼,模型

来源: 防灾减灾工程学报 2019年02期

年度: 2019

分类: 基础科学,工程科技Ⅱ辑

专业: 地质学,建筑科学与工程

单位: 同济大学地下建筑与工程系,同济大学岩土及地下工程教育部重点实验室,上海市政工程设计研究总院(集团)有限公司,同济大学土木工程防灾国家重点实验室

基金: 国家重点研发计划项目(2018YFC1504305,2018YFC0809602,2017YFC1500703),国家自然科学基金项目(51678438),上海市青年科技启明星计划项目(17QC1400500),上海市科学技术委员会(18DZ1205103)资助

分类号: TU435

DOI: 10.13409/j.cnki.jdpme.2019.02.007

页码: 244-249+257

总页数: 7

文件大小: 1608K

下载量: 241

### 相关论文文献

- [1].Quantitative temperature imaging at elevated pressures and in a confined space with CH_4/air laminar flames by filtered Rayleigh scattering[J]. Chinese Physics B 2020(02)

- [2].The axisymmetric Rayleigh waves in a semi-infinite elastic solid[J]. Theoretical & Applied Mechanics Letters 2020(02)

- [3].An analytical study on the Rayleigh wave generation in a stratified structure[J]. Applied Mathematics and Mechanics(English Edition) 2020(07)

- [4].旋转Rayleigh梁在轴向力下的参数稳定性[J]. 应用力学学报 2020(05)

- [5].Rayleigh分布型两部件串联系统的统计分析[J]. 延安大学学报(自然科学版) 2017(02)

- [6].Rayleigh-type wave propagation through liquid layer over corrugated substrate[J]. Applied Mathematics and Mechanics(English Edition) 2017(06)

- [7].Propagations of Rayleigh and Love waves in ZnO films/glass substrates analyzed by three-dimensional finite element method[J]. Chinese Physics B 2017(08)

- [8].Phased Array Beam Fields of Nonlinear Rayleigh Surface Waves[J]. Chinese Physics Letters 2016(07)

- [9].旋转Rayleigh梁的自由振动及失稳特性[J]. 应用力学学报 2020(03)

- [10].Phase Effects of Long-Wavelength Rayleigh–Taylor Instability on the Thin Shell[J]. Chinese Physics Letters 2020(02)

- [11].Sub-Rayleigh imaging via undersampling scanning based on sparsity constraints[J]. Chinese Physics B 2017(02)

- [12].Modified Rayleigh Distribution of Wave Heights in Transitional Water Depths[J]. China Ocean Engineering 2016(03)

- [13].Convection in the Rayleigh-Bénard Flow with all Fluid Properties Variable[J]. Journal of Thermal Science 2011(05)

- [14].酸性磺酞类染料共振Rayleigh散射光谱法测定奈替米星[J]. 西南大学学报(自然科学版) 2011(11)

- [15].Application of multi-channel two-dimensional transient Rayleigh wave exploration in goaf detection[J]. Global Geology 2010(01)

- [16].一种新的Rayleigh-Normal仿真模型[J]. 湖南工程学院学报(自然科学版) 2010(04)

- [17].Numerical simulation of Martian historical dynamo:Impact of the Rayleigh number on the dynamo state[J]. Science in China(Series D:Earth Sciences) 2009(03)

- [18].Phase dispersion of Raman and Rayleigh-enhanced four-wave mixings in femtosecond polarization beats[J]. Chinese Physics B 2009(06)

- [19].基于Rayleigh波法的浅埋混凝土基础无损检测方法研究[J]. 西部交通科技 2020(04)

- [20].多叉指Rayleigh波器件的建模及特性研究[J]. 压电与声光 2019(04)

- [21].Rayleigh分布型n部件串联系统的参数估计[J]. 贵州大学学报(自然科学版) 2017(02)

- [22].Sub-Rayleigh limit imaging via intensity correlation measurements[J]. Chinese Physics B 2015(04)

- [23].Rayleigh波作用下埋地连续管道地震响应分析[J]. 南京工业大学学报(自然科学版) 2020(06)

- [24].Numerical simulation for recognition of coalfield fire areas by Rayleigh waves[J]. International Journal of Mining Science and Technology 2013(01)

- [25].关于复正规矩阵的Rayleigh商[J]. 重庆理工大学学报(自然科学) 2013(06)

- [26].High-resolution Rayleigh wave phase velocity maps from ambient noise tomography in North China[J]. Earthquake Science 2012(03)

- [27].Empirical Bayes Test for the Parameter of Rayleigh Distribution with Error of Measurement[J]. Communications in Mathematical Research 2011(01)

- [28].Rayleigh信道下双门限协作频谱感知研究[J]. 计算机仿真 2010(06)

- [29].Rayleigh Channel Estimation Based on Particle Filter with Simulated Annealing Algorithm[J]. Wuhan University Journal of Natural Sciences 2009(02)

- [30].High-Frequency Rayleigh-Wave Method[J]. Journal of Earth Science 2009(03)

本文来源: https://www.lunwen66.cn/article/04ca5feef7bc60b28fac46f9.html