# Mg/NiTi复合材料的制备及阻尼性能

### 论文摘要

采用Mg粉的无压熔渗法制备Mg/NiTi复合材料以提高多孔NiTi合金的强度和阻尼性能。通过OM、SEM、EDS和XRD分析Mg/NiTi复合材料的显微组织结构,采用压缩实验分析其抗压强度、吸能能力,采用热机械分析仪分析其内耗和存储模量。结果表明:经Mg粉无压熔渗后,多孔NiTi合金的孔隙被Mg填充,其孔隙率由原来的50.38%下降至5.6%,且Mg与NiTi合金的界面结合良好。多孔NiTi合金主要由B2奥氏体相和B19′马氏体相及少量Ni3Ti相和NiTi2相组成;Mg/NiTi复合材料除增加了熔渗的Mg相外,还新生成了Mg2Ni相。Mg的渗入未改变多孔NiTi合金相变行为,但提高了相变温度。Mg/NiTi复合材料的抗压强度可达554MPa,较多孔NiTi合金提高了61%,压缩断裂方式也由多孔NiTi合金的孔壁崩塌断裂转变为Mg/NiTi复合材料的剪切断裂。Mg/NiTi复合材料的吸能较多孔NiTi合金有大幅提高。同时,Mg/NiTi复合材料的内耗值有所增加,而存储模量大幅提高,整体呈现出更佳的阻尼性能。

### 论文目录

- 1 实验材料及方法

- 2 结果与讨论

- 2.1 Mg/NiTi复合材料的显微结构

- 2.2 Mg/NiTi复合材料的相组成及相变行为

- 2.3 Mg/NiTi复合材料的力学性能及吸能能力

- 2.4 Mg/NiTi复合材料的阻尼特性

- 3 结论

### 文章来源

类型: 期刊论文

作者: 徐吉林,陶寿晨,肖奇飞,罗军明,张剑平,刘勇

关键词: 形状记忆合金,复合材料,无压熔渗,阻尼,能量吸收

来源: 复合材料学报 2019年03期

年度: 2019

分类: 工程科技Ⅰ辑

专业: 材料科学

单位: 南昌航空大学材料学院,南昌大学江西省轻质高强结构材料重点实验室

基金: 国家自然科学基金(51101085),航空科学基金(2015ZF56027,2016ZF56020),江西省轻质高强结构材料重点实验室开放基金(20171BCD40003)

分类号: TB33

DOI: 10.13801/j.cnki.fhclxb.20180911.004

页码: 654-660

总页数: 7

文件大小: 554K

下载量: 167

### 相关论文文献

- [1].Experimental investigation of the cyclic degradation of the one-way shape memory effect of NiTi alloys[J]. International Journal of Minerals Metallurgy and Materials 2019(12)

- [2].Effect of Ni Interlayer on Cavitation Erosion Resistance of NiTi Cladding by Tungsten Inert Gas(TIG)Surfacing Process[J]. Acta Metallurgica Sinica(English Letters) 2020(03)

- [3].限空间自蔓延法制备多孔NiTi合金及性能表征[J]. 稀有金属材料与工程 2020(03)

- [4].Elastocaloric effect and mechanical behavior for NiTi shape memory alloys[J]. Chinese Physics B 2018(10)

- [5].NiTi合金伪弹性退化规律及尺度效应的试验研究[J]. 实验力学 2016(05)

- [6].A study on poly(N-vinyl-2-pyrrolidone) covalently bonded NiTi surface for inhibiting protein adsorption[J]. Progress in Natural Science:Materials International 2016(06)

- [7].NiTi形状记忆合金回复应力-温度模型改进与实验研究[J]. 稀有金属材料与工程 2017(01)

- [8].NiTi形状记忆合金热变形机理研究[J]. 世界有色金属 2020(09)

- [9].NiTi合金力学和阻尼性质研究及伪弹性退化分析[J]. 应用力学学报 2019(01)

- [10].Morphology evolution and crystallographic feature of Nb nanowire in an in-situ NiTi-Nb nanocomposite[J]. Rare Metals 2014(05)

- [11].多孔NiTi合金制备的研究现状[J]. 热处理技术与装备 2013(01)

- [12].Surface Modification of NiTi Alloy via Cathodic Plasma Electrolytic Deposition and its Effect on Ni Ion Release and Osteoblast Behaviors[J]. Plasma Science and Technology 2013(07)

- [13].Fine-Grained Bulk NiTi Shape Memory Alloy Fabricated by Rapid Solidifcation Process and Its Mechanical Properties and Damping Performance[J]. Journal of Materials Science & Technology 2013(09)

- [14].Deformation Mechanism of Hot Spinning of NiTi Shape Memory Alloy Tube Based on FEM[J]. Journal of Wuhan University of Technology(Materials Science Edition) 2012(05)

- [15].NiTi合金爆炸焊接试验分析[J]. 焊接学报 2010(12)

- [16].Surface treatment of NiTi shape memory alloy by modified advanced oxidation process[J]. Transactions of Nonferrous Metals Society of China 2009(03)

- [17].NiTi形状记忆合金应变传感特性分析[J]. 哈尔滨工业大学学报 2009(11)

- [18].Characterization of PEG-Like Macromolecular Coatings on Plasma Modified NiTi Alloy[J]. Plasma Science and Technology 2008(02)

- [19].NiTi非晶薄膜的径向分布函数及结构分析[J]. 理化检验(物理分册) 2008(05)

- [20].NiTi合金的第一性原理研究[J]. 物理学报 2008(11)

- [21].NiTi合金电化学抛光工艺[J]. 材料保护 2008(07)

- [22].NiTi形状记忆合金电阻特性研究[J]. 建筑材料学报 2008(05)

- [23].Antibacterial ability and cytocompatibility of Cu-incorporated Ni–Ti–O nanopores on NiTi alloy[J]. Rare Metals 2019(06)

- [24].Microstructure and corrosion behavior of NiTi shape memory alloys sintered in the SPS process[J]. International Journal of Minerals Metallurgy and Materials 2019(10)

- [25].NiTi形状记忆合金丝拉伸力学行为的试验研究[J]. 建筑技术 2014(10)

- [26].计及相变与塑性的NiTi形状记忆合金循环伪弹性特性描述[J]. 应用数学和力学 2014(08)

- [27].Microstructural Evolution of Plastic Deformation of NiTi Shape Memory Alloy at Low Temperature[J]. Journal of Wuhan University of Technology(Materials Science Edition) 2013(05)

- [28].医用多孔NiTi合金微波烧结的初步探讨[J]. 材料导报 2012(S1)

- [29].多孔NiTi形状记忆合金的制备及性能[J]. 材料工程 2011(03)

- [30].基于NiTi形状记忆合金精密微泵的设计[J]. 科技信息 2011(29)

本文来源: https://www.lunwen66.cn/article/895fa6c33d3f640e0f3d1d8b.html